## Slide 1
e- cloud simulations
C.Octavio Domínguez, Giovanni Rumolo, Frank Zimmermann
Thanks to
Humberto Maury Cuna
26th November 2010 - e- cloud simulations

## Slide 2
2
Contents
26th November 2010 - e- cloud simulations
SPS benchmarking :
  SEY scan for different bunch spacing and reflection coefficient
  Vacuum pipe shape study
  Emittance scan
Plans  Discussion:
  Further cross check with Humberto
  Plan for LSS3 simulation; Memory effect
  Plan for coupled-bunch wake field

## Slide 3
3
26th November 2010 - e- cloud simulations
1) SPS benchmarking

## Slide 4
4
SPS - Introduction
26th November 2010 - e- cloud simulations
- Goal: To find onset multipacting SEY for several input parameters

## Slide 5
5
26th November 2010 - e- cloud simulations
SPS - Introduction
The standard parameters:
  Bunch spacing = 50 ns
  Energy = 450 GeV (SPS extraction)
  R = 0.7
  Shape: Elliptical approach of the electron cloud monitor at SPS:
  emax = 230 eV
  Gas pressure = 9 nTorr
  Beam size: The one at the electron cloud monitor at SPS (eNx, Ny = 3.0 mm)
      sx = 0.9 mm
      sy = 0.4 mm
      sz = 11.8 cm
  Nb = 1.1 · 1011 ppb
24.3 mm
70.0 mm

## Slide 6
6
26th November 2010 - e- cloud simulations
SPS – SEY scan
Bs [ns] | R | onset
25 | 0.5 | 1.4
50 | 0.5 | 1.8
75 | 0.5 | 2.3
25 | 1.0 | 1.3
50 | 1.0 | 1.6
75 | 1.0 | 1.9
24.3 mm
70.0 mm
e- cloud monitor (elliptical approach)
sx= 0.9 mm; sy= 0.4 mm; sz= 11.8 cm;
emax= 230 eV; Nb=1.1 1011 ppb; P = 9 nTorr;

## Slide 7
7
26th November 2010 - e- cloud simulations
SPS – SEY scan

## Slide 8
8
26th November 2010 - e- cloud simulations
1.2) Vacuum pipe shape

## Slide 9
9
26th November 2010 - e- cloud simulations
SPS – Pipe shape
24.3 mm
47.15 mm
24.3 mm
47.15 mm
70.0 mm
70.0 mm

## Slide 10
10
26th November 2010 - e- cloud simulations
SPS – Pipe shape
sz= 11.8 cm; bs = 50 ns; emax= 230 eV;
Nb=1.1 1011 ppb; P = 9 nTorr; R = 0.7;
Pipe shape | sx[mm] | sy[mm] | sx[m] | sy,sz [m] | onset
e- cloud monitor (Elliptical) | 0.9 | 0.4 | 0.07 | 0.0243 | 1.7
Elliptical | 0.9 | 0.4 | 0.07 | 0.04715 | 1.3
Round | 0.9 | 0.4 | 0.07 | 0.07 | 1.5
Elliptical | 0.9 | 0.4 | 0.04715 | 0.0243 | 1.7
Round | 0.9 | 0.4 | 0.0243 | 0.0243 | 1.6
MBA (Elliptical) | 0.89947 | 0.460687 | 0.078 | 0.01925 | 2.0?
MBB (Elliptical) | 0.756129 | 0.670483 | 0.066 | 0.2575 | <1.7
LHC type (Elliptical) | 1.0 | 1.0 | 0.022 | 0.018 | X

## Slide 11
11
26th November 2010 - e- cloud simulations
1.3) Emittance scan

## Slide 12
12
26th November 2010 - e- cloud simulations
SPS – e scan
bs = 50 ns; emax= 230 eV; Nb=1.1 1011 ppb; P = 9 nTorr;
R = 0.7;
eNx,Ny [mm] | sx [mm] | sy [mm] | onset
1.5 | 0.78912 | 029059 | 1.7?
2.5 | 0.893224 | 0.37515 | 1.7
3.0 | 0.940968 | 0.410956 | 1.7
3.5 | 0.986403 | 0.443883 | 1.7
4.5 | 1.07151 | 0.503317 | 1.7?
5.5 | 1.15033 | 0.556437 | 1.7?
24.3 mm
70.0 mm
e- cloud monitor (elliptical approach)

## Slide 13
13
26th November 2010 - e- cloud simulations
SPS benchmarking – conclusions
e- cloud simulation for SPS bending magnets are being redone exploring different
parameters
Agreement (apparently) with previous simulations carried out by Giovanni
Round shape option  Worse results
Emittance scan for different LHC type of beams  Very small differences (negligible)
To do:
  Drifts
  Quadrupoles
  Modify code to simulate an elliptic/rectangular shape for a better approach (already
  succeeded once by D. Schulte)
Questions for discussion:
  emax dependence of SEY
  b functions at the e- cloud monitor, i.e. beam size
  Differences between SPS and LHC simulations

## Slide 14
14
26th November 2010 - e- cloud simulations
2) Plans

## Slide 15
15
26th November 2010 - e- cloud simulations
  2.1) Further cross check with Humberto

## Slide 16
16
26th November 2010 - e- cloud simulations
  2.2) LSS3 simulation; Memory effect

## Slide 17
17
LSS3 - Motivation
26th November 2010 - e- cloud simulations
The biggest problems for e- cloud were found in the LSS3 section
That makes interesting to explore it in more detailed

## Slide 18
18
26th November 2010 - e- cloud simulations
Vincent Baglin

## Slide 19
19
26th November 2010 - e- cloud simulations
2.3) Coupled-bunch wake field