## Slide 1
Plans and goals of the scrubbing run
G. Arduini, G. Iadarola, G. Rumolo
With input from: V. Baglin, H. Bartosik, Ph. Baudrenghien, O. Dominguez, B. Goddard, W. Höfle, E. Métral, B. Salvant, L. Tavian, et al.

## Slide 2: Scrubbing history of LHC arcs
dmax decreased from the initial 2.1 to 1.52 in the arcs after approximately 50h machine time with 25ns beams in 2011 (injected nominal and degraded)
It was found to be slightly higher (1.65) in 2012, but it has already decreased to 1.55 at the end the injection tests (4h beam time, 1h between measurements)
25ns threshold @450 GeV
25ns threshold @3.5 TeV
29/06
07/10
24-25/10
14/10
50ns
10/07
/2012
3w p operation (50ns) 2011 + ions + Winter shut-down + 3m operation (50ns) 2012
4 hours
dmax

## Slide 3: Effect of winter stop
Beam 1
Beam 2
Beam 2 - October 24, 2011
Deterioration in SEY confirmed by worse beam lifetime
July 10, 2012
Beam observations
H. Bartosik

## Slide 4: Aims of the scrubbing run and 25 ns e-cloud MDs
Collect additional information on the evolution on the Secondary Electron Yield as a function of the electron dose when low(er) SEY are achieved to determine the expected length of the scrubbing post LS1 for operation at 25 ns.
Benchmark simulations and test scenarios for the optimization of the beams (trains length, bunch intensity) and beam parameters (bunch length and transverse emittance) to enhance scrubbing dose rates.
Further reduce the SEY in the arcs and straight sections to allow ramping to 4 TeV at least a few hundred bunches for beam-beam studies and UFO studies during MD blocks 3-4)
In parallel learn on possible other differences 25 ns vs. 50 ns for heating, UFOs (and UFO conditioning)
Study (during MD block 3-4) the electron cloud build-up at 4 TeV and interplay with photoemission. In parallel learn on possible other differences 25 ns vs. 50 ns for heating, UFOs (and UFO conditioning)

## Slide 5: Choice of bunch intensity
Effect of bunch intensity
Scan in bunch intensity at SEYmax=1.55
Max scrubbing dose @about 8 x 1010 ppb
(however, only 10% larger than at 1.3 x 1011 ppb)
Threshold value for electron cloud build up
Heat load 20% lower than at 1.3 x 1011 ppb

## Slide 6: Choice of bunch intensity
Effect of bunch intensity
Scan in bunch intensity at SEYmax=1.55
Electron distribution in the dipole chamber:
  The central density is higher for lower intensities
  The two stripes move further out with higher intensities
Lower intensity beams also tend to be more unstable due to larger central densities they generate
When injecting higher intensities, bunches at the end of the trains lose and eventually the whole region ±1cm around the center of the chamber is swept with electrons
Electron distribution

## Slide 7: Scrubbing evolution
Ideal bunches
Effect of filling scheme  Scan in SEY at nominal bunch intensity
Degraded bunches (as from last fill)

## Slide 8: Scrubbing run requirements
Requirements for the scrubbing run:
  In the injectors:
    25 ns beam with ~1.2-1.3x1011 p/bunch with nominal emittance (possibly <3 mm)
    Trains of 288 bunches
    We could possibly profit of the low gamma transition optics (Q20) beam from SPS. Preferred.
During the scrubbing run and 25 ns tests:
    Experimental Solenoids and Dipoles should be ON. The previous 25 ns tests were performed with the experimental magnets ON. The polarity of the LHCb dipole should be positive.
    Injection kicker solenoids should be ON. Switch them OFF when long periods without injection in order to scrub the kicker area.
    Vacuum interlock levels should be temporarily increased to few 10-6 mbar (from 4x10-7 mbar) where and if needed and compatibly with machine and experiment protection requirements

## Slide 9: Scrubbing run constraints
We do not expect issues related with intensity ramp-up related to machine protection (Estored 25 ns beam@450GeV~0.2 Estored-50 ns beam@4Tev) but monitoring of:
  RF and damper HOM
  MKI vacuum and temperatures
  BSRT temperatures
  Collimator temperatures
TDI:
  Must be moved in parking position (110 mm gap) once the filling is stopped for periods longer than 15 minutes.
  Monitoring of vacuum and temperatures will be required

## Slide 10: Potential issues
Vacuum in the injection kicker (limiting factor for Beam 2 last year) area particularly Beam 2 slowing down the injection process
Flashover of the kickers (a MKI in point 8 is going to be replaced in order to lift the limitation in the maximum number of bunches that can be injected)
Performance and robustness of the consolidated BSRT mirror
these were the main reasons for postponing the scrubbing run and precede it by a 50 ns intensity ramp-up after the technical stop
these might determine the efficiency of the scrubbing run and the achievable performance at 4 TeV (e-cloud wise)

## Slide 11: Filling schemes for the scrubbing run
Separation:
  Between PS trains: 250 ns. To give some margin in the SPS (non nominal inj. Kicker rise-time and avoid starting with edge bunches with reduced intensity)
  Between SPS trains: 925 ns
G. Iadarola, D. Jacquet
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb = 2100+1 pilot "25ns_2100b_30inj_2012spare"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb = 2460+1 pilot "25ns_2460b_18inj_2012spare"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb = 2604+1 pilot "25ns_2604b_13inj_2012spare"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb = 2604+1 pilot "25ns_2604b_10inj_2012spare"
25 ns slot number
Aim to start with that

## Slide 12: Filling schemes for the scrubbing run
Depending on the progress, we will then switch to more optimized filling patterns
G. Iadarola, D. Jacquet
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb= 2388+1 pilot - “25ns_2388b_27inj_2012"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb= 2604+1 pilot - "25ns_2604b_17inj_2012"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb= 2676+1 pilot - "25ns_2676b_13inj_2012"
0
500
1000
1500
2000
2500
3000
3500
0
0.5
1
1.5
Nb= 2748+1 pilot - "25ns_2748b_11inj_2012"
25 ns slot number

## Slide 13: Scrubbing run plan (all at 450 GeV!)
Thu 4/10 08:00-12:00: Setting-up of the injection of 288 bunches with 25 ns beams for Beam 1 and in particular for Beam 2 (not done this year)
Thu 4/10 12:00-14:00: Damper setting-up (injection of trains of 12 bunches)
Thu 4/10 14:00 – Sun 7/10 12:00
  Go through the filling schemes and accumulate electron dose
  The criterion for dumping a fill will be determined according to the observed heat load “lifetime” and filling time. In any case bunch intensities lower than 0.2-0.3x1011 will lead to dumps (LSS6 BPMs)
Sun 7/10 – 12:00-20:00. Studies (in order of decreasing priority):
  Chromaticity threshold below which the beam is unstable with trains of 72 (or more) bunches
  Emittance blow-up for machine filled with trains of 72 bunches
  e-cloud build-up dependence on bunch length
Sun 7/10 20:00-24:00: Filling pattern to determine SEY in straight sections
Mon 8/10 00:00 Start of MD3

## Slide 14: Scrubbing run plan (all at 450 GeV!)
Thu 4/10 08:00-12:00: Setting-up of the injection of 288 bunches with 25 ns beams for Beam 1 and in particular for Beam 2 (not done this year)
Thu 4/10 12:00-14:00: Damper setting-up (injection of trains of 12 bunches)
Thu 4/10 14:00 – Sun 7/10 12:00
  Go through the filling schemes and accumulate electron dose
  The criterion for dumping a fill will be determined according to the observed heat load “lifetime” and filling time. In any case bunch intensities lower than 0.2-0.3x1011 will lead to dumps (LSS6 BPMs)
Sun 7/10 – 12:00-20:00. Studies (in order of decreasing priority):
  Chromaticity threshold below which the beam is unstable with trains of 72 (or more) bunches
  Emittance blow-up for machine filled with trains of 72 bunches
  e-cloud build-up dependence on bunch length
Sun 7/10 20:00-24:00: Filling pattern to determine SEY in straight sections
Mon 8/10 00:00 Start of MD3

## Slide 15: Scrubbing run plan (all at 450 GeV!)
Thu 4/10 08:00-12:00: Setting-up of the injection of 288 bunches with 25 ns beams for Beam 1 and in particular for Beam 2 (not done this year)
Thu 4/10 12:00-14:00: Damper setting-up (injection of trains of 12 bunches)
Thu 4/10 14:00 – Sun 7/10 12:00
  Go through the filling schemes and accumulate electron dose
  The criterion for dumping a fill will be determined according to the observed heat load “lifetime” and filling time. In any case bunch intensities lower than 0.2-0.3x1011 will lead to dumps (LSS6 BPMs)
Sun 7/10 – 12:00-20:00. Studies (in order of decreasing priority):
  Chromaticity threshold below which the beam is unstable with trains of 72 (or more) bunches
  Emittance blow-up for machine filled with trains of 72 bunches
  e-cloud build-up dependence on bunch length
Sun 7/10 20:00-24:00: Filling pattern to determine SEY in straight sections
Mon 8/10 00:00: Start of MD3

## Slide 16: Preparation for the scrubbing run
Transverse feedback (D. Valuch):
  Larger bandwidth of the transverse feedback to be tested ahead of the scrubbing run (few hours in stable beams) during the 50 ns run (operational development)
BPM in LSS6 (R. Jones):
  After the technical stop it might be possible to put in operation the new logic for the LSS6 BPMs not taking into account of bunch trajectories when they are below sensitivity threshold (being tested)  could be an issue if too many bunches end up below detection threshold

## Slide 17: Regular measurements during scrubbing
Chromaticity measurement before starting any high intensity fill
Beam measurements
  Transverse emittance:
    LHC: Wire scanner (possible with 300 bunches?), BSRT in fast scan mode, BGI
    SPS: Wire scanner in bunch-by-bunch mode at SPS extraction
  Bunch-by-bunch intensity (FBCT) and total intensity (DCBCT)
  Transverse oscillations:
    BBQ and Hump buster
    ADT pickup (bunch-by-bunch position)
    Head-tail monitor
    BLM bunch by bunch
  Longitudinal parameters:
    Bunch length evolution
    Longitudinal beam spectra
Electron cloud measurements
  Heat load in the arcs, stand-alone and triplets
  Bunch-by-bunch RF stable phase
  Vacuum pressures (selection of gauges to be defined with vacuum team)
  Electron flux measurements from BPMs (available?)

## Slide 18: 4 TeV tests

## Slide 19: 4 TeV tests
2 ramps  4h flat top each ramp (up to 400b. for first, 800b. for the second)
Criterion for the choice of the filling pattern (at the end of the scrubbing run Number of trains of 72 (or larger) bunches that do not show: ) 
  Sign of instability /important blow-up at injection
  Pressures below 10-7 mbar
  Heat loads due to e-cloud in the range of a few 100 mW/m/aperture, or lower
Interest in ramping 25ns beams to 4 TeV:
  Study (during MD block 3-4) the electron cloud build-up at 4 TeV (interplay with photoemission, further scrubbing). In parallel learn on possible other differences 25 ns vs. 50 ns for heating, UFOs (and UFO conditioning)
  Long-range beam-beam MDs
  Experiments