## Slide 1: Bunch-spacing scan for two different bunch profiles at 7 TeV
Humberto Maury Cuna
E-cloud Simulation Meeting
February 15th, 2012

## Slide 2: Simulation parameters for 7 TeV
Bunch spacing | Bunch intensity | SEY | R | Bunch profile | rms Bunch length
5 ns – 50ns | 6 x 1010 1.15 x 1011 1.7x 1011 2.3 x 1011 | 1.1 1.7 | 0.5 | Gaussian Flat | 7. 55 cm 11.8 cm

## Slide 6: Conclusions
The Gaussian bunch profile gives higher heat load values than the flat bunch profile.
Small bunch spacing gives considerable high heat load values
For SEY = 1.7 there is an exponential dependence of the heat load with the inverse of the bunch spacing.
Future work: Flat profile with same Gaussian RMS bunch length (7.55 cm)

## Slide 7
Thank you for your attention